A GPS Time-Tagging Test Stand
A. Ferguson
R. Sobin
US Analysis Meeting @ CWRU
October, 2013

---
The CWRU “Time Machine”

---
Current Setup

---
Timing Histograms
- The variance of the real time difference between test and reference receivers changes between tests.
- Why?

---
Thermal Sensitivity (1/3)
- We noticed that the oscillator calibration varied over the course of a run.
- This is suspiciously close to the duty cycle on the lab's air conditioning.
Oscillator
 Calibration
Real Time
Difference

---
Thermal Sensitivity (2/3)
Putting the receiver and test stand in a temperature controlled chamber greatly reduces the variance of the oscillator calibration.

---
Thermal Sensitivity (3/3)
To determine the “best case” variance we varied the temperature of the receivers between -5 and 30 C.

---
Conclusions
- We're on our way to being able to say something along the lines of:
- “Given the conditions in the field, we are confident we can report the receiver offsets to within … nanoseconds.”

---
“Backup Slides”

---
Snapshot @ 10-10-2013 12:36 UTC